## Slide 1
OpenTURNS
G. Blondet, Phimeca Engineering SA
‘HPC and Uncertainty Treatment – Examples with Open TURNS and Uranie’
EDF – Phimeca – Airbus Group – IMACS – CEA
PRACE Advanced Training Center – May, 10-12, 2021

## Slide 2: Outline
Overview of OpenTURNS (OT)
Doc and Users
OT in pictures
OT in practice

## Slide 3: Outline
Overview of OpenTURNS
  What is OpenTURNS?
  Uncertainty methodology
  OpenTURNS features
  Uncertainty quantification with OpenTURNS
  Innovations
Doc and Users
OT in pictures
OT in practice

## Slide 4: What is Open TURNS?
Partnership since 2005 between:
  EDF - R&D EADS - Innovation Works Phimeca IMACS (since 2014)
Open-source initiative to Treat Uncertainties, Risks’N Statistics
  Open-source platform for uncertainty treatment
  Uncertainty propagation
  Uncertainty quantification and Uncertainty ranking
  Meta-model building
  working on Unix/Linux platform and Windows (since 2010)
Open TURNS includes:
  C++ scientific library including the methods for performing uncertainties treatment (statistic, reliability, etc.);
  A python module : simplify your work with an interpreted language;
  A complete documentation;
  A website: http://openturns.github.io/

## Slide 5: Uncertainty methodology (1/2)
Global Methodology of Treatment of Uncertainties
  developed first at EDF R&D in 1990 and then improved by contributions from other companies
Step A : Study Specification
Uncertainty sources, model, variable of interest and criteria
Step B : Uncertainty Quantification
Joint probability density function of the input uncertain parameters modeling
Step C : Uncertainty Propagation
Variable of interest uncertainty assessment
Step C’ : Uncertainty Ranking / sensitivity analysis
Uncertainty sources ranking with respect to their influence on the variable of interest uncertainty

## Slide 6: Uncertainty methodology (2/2)
Decision criterion
Ex: Probability < 10-b
Correcting model
Real system
f R(x)
Input variables
Variables : x
Parameters : q
Variables of interest
Y = f(x,q)
Y R = f R(x)
Step A : Study specification
Numerical model
f(x,q)
Step C : Uncertainty Propagation
Step C’ : Sensitivity analysis
Step B :
Uncertainty quantification
Probabilistic model
(joint distribution)
Direct methods, statistics, expert assessment
Variables observed
Yobs(xi)
Step B’: Calibration / Validation
Quantity of interest
Ex : variance, probability

## Slide 7: OpenTURNS features
Code linked to OpenTURNS
  Interface with python functions  to perform complex wrappers without compilation + parallelization functionalities
  Standard Interface for the wrappers of any complexity (distributed wrapper, binary data) development requiring the development of an external wrapper
  SalomeMeca compatible  software including the 3 components to perform a mechanical and probabilistic data models coupling (linked to YACS)
  GUI of OpenTURNS within SalomeMeca
  FE modeling
  Probabilistic modeling
  Mechanical modeling

## Slide 8: Uncertainty quantification with OpenTURNS
Estimation from data :
      Distribution fittings (parametric or not)
      Validation Tests (quantitative or graphical)
      Estimation of the dependence : copula, correlation coefficient
      Regression
Analytical modeling of joint distributions of dimension :
      Combination Marginals + Copula
      Parametric distributions of dimension
      Truncated distributions
      Stochastic process
      Non parametric distribution of dimension : kernel fitting (n), Sklar Copula
      Linear combination of PDF
      Linear combination of random variables
      Random sum of independent discrete variables according to a Poisson process
      Etc.

## Slide 9: Uncertainty propagation with OpenTURNS
Sampling data:
  Random generator
      Stratified design of experiment
      Latin Hypercube Sampling
      Low Discrepancy Sequence
      Markov chain
Probability estimation:
      Isoprobabilistic transformation
      FORM / SORM
      Monte Carlo simulation
      Importance simulation
      Directional simulation
      Latin hypercube simulation
      Simulation algorithms

## Slide 10: Uncertainty ranking with OpenTURNS
Ranking and sensitivity analysis:
  Importance factor from Taylor decomposition
  Ranking from correlation
  Sensitivity analysis
  Importance factor from reliability methods
Tools
  Optimization algorithm
      Response surface:
        Parametric approximation
        Functional chaos expansion
        Kriging
      Graph
and Modules…

## Slide 11: Innovative and recently implemented algorithms
  the most recent and efficient algorithms of non uniform distribution generation
      Ziggurat method (2005) for the normal distribution
      sequential reject algorithm (1993) for the binomial distribution,
      Tsang & Marsaglia method (2000) for the gamma distribution,
      Lebrun algorithm (2012) for the MultiNomial distribution,
  the most recent algorithms for evaluating the CDF
      Marsaglia algorithm for the exact statistics of Kolmogorov (2003),
      Benton et Krishnamoorthy algorithm for the distributions non centered Student and non centered Chi2 (2003).
  PhD results
      Sparse chaos expansion polynomials : G. Blatman (EDF/R&D/MMC) (2010)
      Accelerated simulation algorithm for the evaluation of low probabilities : M. Munoz (EDF/R&D/MRI) : (current dev)
      Copulas for order statistics distributions: R. Lebrun (EADS) , Richard Fischer (EDF) (2013)

## Slide 12: Outline
Overview of OpenTURNS
Doc and Users
OT in pictures
OT in practice

## Slide 13: OpenTURNS: Doc and Users
Several guides intended for users
      Installation : Windows/Linux, from anaconda or sources
      API Reference : Python docstring of most of the objects, arguments and methods in OpenTURNS and available in HTML.
      Examples Guide : application of the whole Global Methodology on classical mechanical examples‏
      Reference Guide : Theory of the methods implemented within OpenTURNS
      Contribute : how to contribute to OpenTURNS, core code, modules …
… and a sympathetic community :
      Openturns.org : official web site
      a particular page share to communicate about the software
      the annual Users Day

## Slide 14: OpenTURNS: Doc and Users
Mailing list for users: users@openturns.org:
  Ask any question relative to the installation and use of Open TURNS
Community tools:
  https://openturns.discourse.group/
  https://gitter.im/openturns/community

## Slide 15: Outline
Overview of OpenTURNS
Doc and Users
OT in pictures
OT in practice

## Slide 16: OpenTURNS in pictures

## Slide 17: OpenTURNS in pictures

## Slide 18: OpenTURNS in pictures

## Slide 19: Outline
Overview of OpenTURNS
Doc and Users
OT in pictures
OT in practice

## Slide 20
Basic commands in OT (1/3)‏
Mathematical objects
Importation of OpenTURNS functionalities

## Slide 21
Basic commands in OT (2/3)‏
Methods
G. Blondet – Maison de la simulation – May, 10-12 2021

## Slide 22
Basic commands in OT (3/3)‏
Methods
Objet relative to the method
« . » between the objet and the method
Name of the method
« () » at the end of the method
G. Blondet – Maison de la simulation – May, 10-12 2021

## Slide 23: Example of uncertainty propagation
L
E, I
p
Bending beam under uniform loading
Maximal displacement
Probabilistic model
parameter | Symbol | Distribution | Mean | Standard Deviation
Length [mm] | L | Lognormal | 5000 | 50
Young modulus [MPa] | E | Lognormal | 30000 | 4500
Inertia [mm4] | I | Lognormal | 109 | 108
Load [N/mm] | p | Lognormal | 10 | 3
G. Blondet – Maison de la simulation – May, 10-12 2021

## Slide 24: Model function
Defining a Function
G. Blondet – Maison de la simulation – May, 10-12 2021

## Slide 25: Defining the derivatives
Centered Finite difference
G. Blondet – Maison de la simulation – May, 10-12 2021

## Slide 26: Defining the probabilistic model
1 – Define the marginals
G. Blondet – Maison de la simulation – May, 10-12 2021

## Slide 27: Defining the probabilistic model
2 – Define the composed distribution
G. Blondet – Maison de la simulation – May, 10-12 2021

## Slide 28: Defining the probabilistic model
2 bis – Define the correlation
If the variables are dependent, a copula can be added.
G. Blondet – Maison de la simulation – May, 10-12 2021

## Slide 29: Propagation using MC simulations
3 - Get input and output
G. Blondet – Maison de la simulation – May, 10-12 2021

## Slide 30: Result of the MC simulation
Estimation of the 4 first moments of the displacement
G. Blondet – Maison de la simulation – May, 10-12 2021

## Slide 31: Histogram and empirical CDF
Graphs on the sample DepMC
G. Blondet – Maison de la simulation – May, 10-12 2021