## Slide 1: OpenTURNS and HPC within SALOME platform O. Mircescu EDF R&D
HPC and Uncertainty Treatment
Examples with OpenTURNS
EDF – PhiMeca – IMACS – Airbus Group – CEA
Prace Advanced Training Center
May 12th 2019

## Slide 2: OUTLINE
Presentation of Salome
Persalys – graphical user interface for OpenTURNS
Step by step example
Persalys – distribution and future evolutions

## Slide 3: Presentation of Salome (1/5)
What’s Salome ?
  Modular simulation platform
  An open framework to build domain specific solutions
  Who is developing Salome ?
  EDF, CEA and OpenCascade partnership

## Slide 4: Presentation of Salome (2/5)
  A middleware providing generic tools for numerical simulations
  Geometry modelling, meshing, field handling and visualization
  Data Exchange Model for interoperability between solvers and tools
  Computation scheduling (YACS)
= SALOME Platform
Computation scheduling
(workflow, distribution)
Complex data processing
(fields, matrix, etc)
3D Modelling
(CAD, meshing, visualization)
+
+

## Slide 5: Presentation of Salome (3/5)
Presentation of YACS
  Distribution of computations on multiple resources
  Parallelism and parametric computation
  Chaining computation nodes
  GUI and APIs for Python and C++

## Slide 6: Presentation of Salome (4/5)
Presentation of JOBMANAGER
  Create, launch and monitor jobs on computer clusters
  Single interface for several batch managers (Slurm, PBS, COORM, OAR, SGE, LSF)
  GUI and APIs for Python and C++
  Jobs can run scripts or YACS schemas

## Slide 7: Presentation of Salome (5/5)
Parametric layer
  Simplified interface for parametric studies
  Uses YACS and JOBMANAGER

## Slide 8: Persalys (1/5)
Graphical user interface for OpenTURNS
Guide the user in a homogeneous environment through the roadmap defined by the global methodology of treatment of uncertainties

## Slide 9: Persalys (2/5)
Persalys is more than a simple GUI !
  Persalys is based on a high level object model (study workflow)
  Persalys includes a layer over OpenTURNS tools.
  Persalys has been designed to mix beginners and advanced users
How can you use it ?
  Standalone binary (persalys)
  In a dedicated salome module (Persalys)
  Can be used in a customized salome module (ASTER STUDY, CFD STUDY)

## Slide 10: Persalys (3/5)
Two complementary ways to pilot Persalys : Python and widgets
The design of Persalys allows a strong relationship between Python scripting and graphical interface (Model/View paradigm).
  Actions you perform on gui can be mapped into a Python representation.
  Load python script and dump python script.
  Start session with graphical interface then continue with script then…
Persalys offers software bricks usable outside a dedicated tool

## Slide 11: Persalys (4/5)
Persalys is an excellent target for High Performance Computing (HPC)
  A large number of independent evaluations
Salome features used by Persalys:
  Manage a catalog of available computation resources
  Make the evaluations parallel and distributed
  Communicate with the batch manager
    Define the job parameters
    Submit and keep track of a job
  Define the execution environment
    Define a working directory
    Copy data from the local workstation to the remote cluster
  Fetch the results

## Slide 12: Persalys (5/5)
SALOME software bricks used by Persalys
  YACS & JOBMANAGER
  GUI Python console widget
  PARAVIS widgets

## Slide 13: a study step by step
Install and configure Salome
Define the function to be studied
Create a model (YACS or python models in the GUI)
Define the laws of input parameters
Choose the type of study (central tendency, etc.)
Choose the execution parameters
Run the study and wait for results
Analyse the results

## Slide 14: Install and configure Salome
Installation steps
  Install Salome on your personal computer
    https://www.salome-platform.org/contributions/edf_products
  Install Salome on the remote cluster
  Make sure you can connect to cluster without typing the password (ssh-copy-id)
  Declare the cluster installation in your local resource catalog (JOBMANAGER module)
1st click
2nd click

## Slide 15: Configure available resources
Salome resources
  Salome has to be installed on every machine you want to use
  You have to declare each installation in your local catalog of resources
  Main parameters:
    Name
    IP adresse
    User name
    Path to Salome installation
    Batch manager

## Slide 16: Define the function to be studied
Identify uncertain parameters – inputs and outputs of your study
Use the python language
  Input parameters must be only float variables
  Return statement must contain only float variables
  The name of the function should be “_exec”
The python function should:
  Generate the input files for the solver based on the input parameters
    Create a specific working directory for each execution of the function
  Launch the solver
  Retrieve the results from the output files of the solver
Test your function

## Slide 17: Example of a study function
Syrthes : thermal radiation solver
h1 T1
Face S1
h2 T2
Face S2
Heat exchange coefficient: h1, h2
Conductivity: lamb
Density: rho
Heat capacity: cp
Heat exchange computation with SYRTHES
def _exec(h1, h2, rho, cp, lamb):
e = Study(h1, h2, rho, cp, lamb)
e.defineWorkDirectory()
if not e.caseExists():
e.prepareCase()
e.runCase()
temp, balance = e.getResults()
return temp, balance

## Slide 18: Create a model
  Open the Persalys module in a Salome session
  Create a new study with a YACS model
  Set the python script in the YACS model

## Slide 19: Define the laws of input parameters
Probabilistic model
User design of experiments

## Slide 20: Choose the type of study

## Slide 21: Run the study and wait for results
Choose
  Computing resource
  Job parameters
    Number of nodes
    Time to execute
    Etc.
  Remote working directory
  Local files to be copied to the remote working directory

## Slide 22: Result analysis tools
Box plots, Cobweb plot, Plot matrix, Scatter plots

## Slide 23: Persalys - Distribution and future evolutions (1/2)
Distribution of SALOME + OpenTURNS platform
  LGPL license for the whole platform (SALOME + OpenTURNS + Persalys)
  Download SALOME platform with OpenTURNS here:
    http://www.salome-platform.org/contributions/copy_of_combs
Persalys is also available stand alone, but without the support for launching on remote resources

## Slide 24: Persalys - Distribution and future evolutions (2/2)
Improvements to come
  Launch, leave and reconnect to a job
  Avoid multiple job submissions for one OpenTURNS study
  Management of a partially executed study
  Management of failed computations

## Slide 25
Questions?